Driving LEDs
Tim Slagle
DorkbotDC
1 Nov 2006

---
LED Hookup
Light Emitting Diode = LED
Run current through LED to light:
+ to – or anode to cathode
Flat side negative; long lead positive
Brightness proportional to current --->
Max 20 mA for typical 5mm LED
(more current = shorter life)
Rechargeable AA has 2400 mAHour so
can run LED for 120 hours=5 days!
1 A = 1000 mA
A=Amp mA=Milliamp
VSOURCE
ILED
+
+
-
-
LED

---
That sounds easy, but...
No current flows when under threshold voltage
Current changes fast with voltage once LED turns on
Voltage needed is probably not the voltage you have, but too much voltage will blow out LED or reduce life
Brightness sensitive to small changes and differences between parts
VF = VLED

---
Solution: Series Resistor
Adding a resistor in series will decrease I vs V slope
Enables higher drive voltages
Reduces sensitivity to voltage and Vthresh variations
Power dissipated in resistor is wasted – bad for batteries
5V
12V
VSOURCE
ILED
+
-
+
-
LED
RLED

---
But which resistor?
Formulas: V=I*R Units: [Volts]=[Amps]*[Ohms]
   and: VSOURCE = VRESISTOR + VLED
Find (or guess) VLED for desired drive current (e.g. 0.02A)
Calc: RLED = (VSOURCE – VLED) / ILED
Check resistor power: PRLED = V*I = (ILED*RLED) * (ILED)
Common resistor powers: 1/8 W, 1/4 W, 1/2 W (W=Watts)
VLED for: Red/Amber Orange/Yellow/Green Green/Blue/White

---
Examples